## Slide 1: CFD F1 MCM

## Slide 2: Model
Variable
  Single or double rear vanes
inlet
outlet
400 mm
100 mm

## Slide 3: Assumption
Tyre fixed
Cannister is ignored
Rear wings is removed for simplicity (actually keep facing issue at one surface with bad facets)
Assuming subsonic – flow is assumed as incompressible

## Slide 4: Mesh

## Slide 5: Boundary condition
Inlet – 25 m/s (this is ramped over 1 s)
Time dependent simulation (Inlet is ramped from 0 to 25 m/s)
Outlet – zero pressure
The rest of boundary is set as wall or zero velocity
Simulation is run in COMSOL 6.1
Time (s)
Inlet velocity (1 is max)

## Slide 6: Result
Total drag (mN) across time
Time (s) | Inlet Velocity (m/s) | Single Vane (mN) | Double Vane (mN)
0.1 | 2.25 | 1.8056 | 1.6785
0.2 | 4.75 | 3.3874 | 3.5279
0.3 | 7.25 | 5.2954 | 5.5656
0.4 | 9.75 | 7.3611 | 7.6892
0.5 | 12.25 | 9.4996 | 9.8611
0.6 | 14.75 | 11.660 | 12.056
0.7 | 17.25 | 13.826 | 14.262
0.8 | 19.75 | 15.992 | 16.472
0.9 | 22.25 | 18.151 | 18.683
1 | 24.75 | 20.236 | 20.819
1.1 | 25 | 20.501 | 21.088

## Slide 7: Fluid Velocity
Single vane
Double vane
Single vane
Double vane
Single vane
Double vane

## Slide 8: Fluid streamline
Single vane
Double vane

## Slide 9: Wall shear stress at the rear (Pa)
Single vane
Double vane

## Slide 10: Pressure Isosurface (Pa)
Single vane
Double vane

## Slide 11: Pressure (Pa)
Single vane
Double vane
Single vane
Double vane

## Slide 12: Comments
The drag seems to be less in single vane (not by much), probably due to the double vane imposes additional flow resistance.
  However, the drag is greatly influenced by mesh
The vanes seems help to orient the pressure so low pressure is nearer to the cannister outlet, which might help to propel the car

## Slide 13: Limitation
Mesh is quite coarse and some facets issue in the surface between the wings and body, this might affect drag calculations and pressure
  Normally we would refine the mesh by halving the size 4x to ensure the results no longer change
  I noticed some parts contains sharp edges, especially in the rear wings, which makes it difficult to import into model,
    For future work, best to merge all the parts (components) in the CAD, using Boolean operator
Assumption of no turbulence